## Slide 1: Privacy Preserving Collaborative IDS for Internet of vehicle networks
Faculty Members: Student Members:
Mrs. Durga Hithesh Y
Mrs. Uma Saurabh Krishnan
Mrs. Anusuya
Mr. Praveen

## Slide 2: Content:
Threat Model
Threat Matrix and Risk Matrix
Baseline Architecture
Model Architecture
Why FHE in FL
Security and Performance Report
HE Schemes

## Slide 3: Problem Statement
Challenges in Internet of Vehicles (IoV)
Increasing Cyber-Attacks on Connected Vehicles: Modern vehicles are vulnerable to in-vehicle network (IVN) exploits (e.g., DoS, Fuzzy, RPM, and Gear spoofing attacks) and V2X wireless threats.
Privacy Concerns in Sharing Vehicle Data: Strict data privacy regulations (e.g., GDPR, CCPA) prevent vehicles from uploading raw telemetry, location history, or sensor logs to centralized servers.
Limitations of Centralized IDS:
  Bandwidth bottlenecks from transmitting massive, continuous streams of high-frequency vehicular data.
  Single point of failure: vulnerability to connection drops in high-mobility environments.

## Slide 4
Proposed Solution: FedIoV
Federated Learning (FL) Framework: Enables collaborative training where vehicles train intrusion detection models locally and only share encrypted model updates (gradients) with the server.
Kolmogorov-Arnold Network (KANConvNet): A lightweight, edge-optimized classifier with learnable activation functions on edges rather than nodes, reducing computational overhead.
Layer-Wise Fully Homomorphic Encryption (FHE): Selectively encrypts only the most sensitive layers of the KAN model during aggregation, resolving the speed limitations of traditional FHE while preserving privacy.

## Slide 5: Project Objectives
Design a Collaborative IDS for IoV: Develop a distributed, cooperative system to detect cyber threats across the fleet without requiring a central database of raw logs.
Preserve Privacy of Vehicle Data: Leverage secure cryptographic channels and Layer-Wise FHE to ensure vehicle telemetry remains private.
Support Distributed Learning Across Vehicles: Build a robust Federated Learning client-server architecture capable of handling vehicle churn, communication drops, and non-IID settings.
Detect Vehicular Cyber Attacks Efficiently: Implement and optimize KANConvNet to detect low-latency attacks (target latency <60<60 ms) on resource-constrained Electronic Control Units (ECUs).

## Slide 6: Threat Model
Step 1 – Set Objectives
Primary Objective: Build a real-time, privacy-preserving Intrusion Detection System (IDS) to secure the Internet of Vehicles (IoV) against cyber-threats.
Security Goals (CIA-P Triad):
  Confidentiality: Protect vehicle network traffic and machine learning model weights from eavesdroppers.
  Integrity: Ensure model updates are not tampered with, and prevent compromised vehicles from injecting malicious updates.
  Availability: Ensure the system can detect and respond to attacks in real-time (under 60ms).
  Privacy: Guarantee raw vehicle telemetry (GPS location, speed, routes) never leaves the on-board unit.

## Slide 7
Step 2 – Visualize
The Architecture (FedIoV / DCANFL):
  Edge Client (Vehicle): Collects local CAN bus traffic →→ extracts a 46-dimensional "timeless" feature vector →→ trains a local KANConvNet model.
  Secure Communication Channel: Vehicle handshakes with the Edge Server using Ed25519 (authentication) and ECDH-P256 (key exchange) to encrypt updates with AES-256-GCM.
  Edge Server (Aggregator): Collects encrypted updates →→ runs Multi-Krum to filter outliers →→ averages updates →→ broadcasts the new global model.
  Layer-Wise FHE (Fully Homomorphic Encryption): Selectively encrypts the most sensitive layer weights of the KAN ConvNet, allowing the server to aggregate them without decrypting them.

## Slide 8
Step 3 – Identify Threats
Threat 1: In-Vehicle Network Attacks (CAN Bus Exploitation)
  Denial of Service (DoS): Attackers flood the CAN bus with high-priority messages, freezing brakes or steering controls.
  Fuzzy / Impersonation Attacks: Attackers inject random or spoofed packets to confuse onboard ECUs.
Threat 2: Byzantine / Poisoning Attacks (Machine Learning Level)
  Model Poisoning: Hacked vehicles upload corrupt model weights during federated training to blind the global model to specific attacks.
Threat 3: Communication Eavesdropping & Privacy Leakage
  Man-in-the-Middle (MitM): Intercepting and modifying model updates in transit.
  Reconstruction Attacks: Eavesdroppers reverse-engineering plaintext model weights to reconstruct raw driving telemetry

## Slide 9
Step 4 – Mitigate
Mitigating In-Vehicle Attacks:
  KANConvNet IDS: Runs locally on the vehicle, analyzing overlapping sliding windows (W=64W=64, S=16S=16) to flag anomalous entropy, payload patterns, or ID frequencies.
Mitigating Federated Poisoning (Byzantine Attacks):
  Multi-Krum & TOPSIS: The edge server calculates distance metrics between updates. Outliers (e.g., poisoned updates from hacked cars) are isolated and discarded.
Mitigating Network & Privacy Threats:
  ECDH + AES-256-GCM: Establishes ephemeral key encryption for all transmissions (perfect forward secrecy).
  Layer-Wise FHE: Fully Homomorphic Encryption is applied only to the most sensitive layers of the KANConvNet, keeping performance fast while guaranteeing cryptographic privacy.

## Slide 10: Threat Matrix
Threat | Description | Mitigation
Data & Model Poisoning | Attacker injects bad data or manipulated gradients | Multi-Krum + TOPSIS
Man-in-the-Middle | Attacker intercepts or modifies updates between client & server | Ed25519 + AES-256-GCM
Backdoor Attack | Attacker inserts hidden triggers that activate malicious behavior | Multi-Krum distance-based filtering
Byzantine Failure | Malicious clients send arbitrary or corrupted updates | Multi-Krum selects top 5 consistent
Privacy Attacks (Inversion/Leakage) | Attacker reconstructs training data from shared gradients | Differential Privacy (σ=1.2, C=1.0)
Denial of Service | Attacker floods server with updates to overwhelm processing | TOPSIS dimensionality reduction

## Slide 11: Dataset Acquisition
Car-Hacking Dataset(HCRL): (1 year ago)
  Scope: Labeled CAN bus traffic from a real Hyundai YF Sonata.
  Size/Type: CSV logs containing CAN-ID, DLC, payload bytes, and injection flags.
  Threat Classes: Normal run, DoS, Fuzzy, RPM, and Gear attacks.
VeReMi Dataset: ( 3 years ago)
  Scope: Kinematic beacon data from V2V communication in VANET simulations.
  Size/Type: 18 kinematic features (positions, speeds, accelerations, headings, noise levels).
  Threat Classes: Benign (BENIGN) and Attack (ATTACK) (falsified kinematic attributes).
3.CICIDS 2017 Dataset: (updated 3 years ago)
  Scope: Network flow-level traffic logs spanning multi-layer V2I and V2N network protocols.
  Size/Type: 78 numeric flow features down-selected to a stable 46-feature network baseline.
  Threat Classes: Benign vs. Attack (DDoS, PortScan, FTP-Patator, SSH-Patator, Web Attacks, etc.)
4.IEEE VTC-CAN Dataset: (last updated 2025)
  Scope: Labeled high-fidelity in-vehicle CAN bus log stream under attack injections.
  Size/Type: CAN frames windowed to 46-dimensional temporal descriptors.
  Threat Classes: Attack-free, DoS attack, Fuzzy attack, and Impersonation attack.

## Slide 12
Justification
Coverage:
  Low-Level IVN Protection: Car-Hacking and IEEE VTC-CAN evaluate anomaly detection on the internal physical ECU bus (message intervals, ID distributions, payload integrity).
  High-Level V2V Protection: VeReMi evaluates system resilience to geographic and kinematic coordinate spoofing or communication misbehavior.
  High-Level V2I/V2N Protection: CICIDS 2017 evaluates broad network-layer threats (DDoS, brute-force exploits, scans) targeting external connectivity.
Realism & Data Heterogeneity: Incorporating these four distinct datasets tests the dataset-agnostic feature engineering layer and the robustness of KANConvNet across high-frequency binary sequences, continuous float vectors, and IP traffic metrics.

## Slide 13: Data Engineering
Challenge: Heterogeneous DatasetsVarying Protocols: CAN bus messages (HEX payloads) vs. V2X beacons (coordinate floats) vs. IP flows (network counts).
Goal: Standardize diverse inputs into a single format so the same neural network (KANConvNet) can be reused.
Solution: Unified Feature Extraction
Sliding Window: Group incoming message streams into a sliding window of size W=64 messages and stride S=16.
Feature Unification: Summarize each window into exactly 46 universal features (numbers).
Unified Pipeline: Creates a dataset-agnostic feature vector x∈R^46 for the classifier model.

## Slide 14: Data Engineering (46-D Feature Mapping)
In-Vehicle Networks (Car-Hacking & IEEE VTC-CAN):
What it measures: High-frequency messages exchanged between internal ECUs.
46-D Feature Breakdown:Payload Stats (16):
Average value & deviation of raw data bytes (b0..b7).
Message Length (2): Average & deviation of Data Length Code (DLC).
Component Identity (26): Active CAN-ID distribution histogram hashed over 24 buckets + dominant ID stats.
Data Entropy (2): Information randomness and non-zero payload ratio.
2. V2X Telemetry Networks (VeReMi):
What it measures: GPS and motion telemetry shared between vehicles.
46-D Feature Breakdown:
Average Motion (18): Position, speed, heading, and sensor noise averages. Fluctuations (18): Standard deviations of kinematic readings over the window.
Derived Forces (5): Total speed magnitude, acceleration force, and heading intensity.
Behavior Stats (5): Spatial coordinates spread, time intervals, and broadcast rates.

## Slide 15: Data Engineering (46-D Feature Mapping)
3. IP Networks (CICIDS 2017):
What it measures: External Internet network traffic flows.
46-D Feature Breakdown:
Transfer Rates (6): Flow duration, bytes/second, packets/second, and average size.
Flow Sizes (12): Total forward/backward data size and packet lengths.
Time Gaps (15): Inter-Arrival Times (IAT) of packet streams.
Control & Headers (13): TCP flags (SYN, ACK, RST) and packet header sizes.

## Slide 16: Data Engineering (Preprocessing)
Data Cleaning Pipeline
Percentile Clipping: Continuous features are clipped at the 0.5th and 99.5th percentiles (using training set bounds) to remove noisy sensor spikes and outliers.
Z-score Standardization: Every feature is scaled to standard bounds.
Safeguarding Against Data Leakage (Anti-Cheating)
Centralized Stratified Split: 70% Train, 15% Validation, 15% Test.
Strict Training Isolation: Mean (μ) and standard deviation (σ) parameters are computed only on the 70% training split.
Evaluation Integrity: The calculated training statistics are locked and then used to scale validation and testing sets

## Slide 17: Non-IID Simulation
1. Fleet Setup & Connectivity Constraints
Simulated Fleet Size (N): N∈{50,100,200} client vehicles, each running KANConvNet in containerized/isolated environments.
Client Sampling Fraction (q): Server selects a random subset of active vehicles at each round (q=0.60 for N=50, q=0.70 for N=100, and q=0.75 for N=200).
Vehicular Churn(P drop): Simulated random client dropout of 5%−20% per round due to tunnel shadowing, signal fading, or moving out of range. Dropped clients can rejoin later.

## Slide 18: Non-IID Simulation
2.Dirichlet Non-IID Partitioning
To model realistic geographic variations where different vehicles encounter different traffic patterns and attack ratios:
Mathematical Split:
Training data is split across clients using a Dirichlet distribution with concentration parameter α=0.3.pc ∼ Dir(α⋅1N) where pc represents the proportion of samples from class c allocated to each of the N clients
Class Skew Effect:
A smaller α leads to higher skew (non-IID conditions).
With α=0.3, some vehicles observe only benign traffic, while others are dominated by a single attack class (e.g., DoS only), forcing the global model to learn from highly heterogeneous client updates.
Centralized Evaluation:
Validation and test splits are kept centralized at the server, ensuring unbiased and global performance metrics.

## Slide 19: Baseline Architecture:
PHASE 1: INITIALIZATION:
1. Role : Central Server
2. Action : Init & Broadcast global model
3. Target : N Vehicles
4. Security : SecureChannel (ECDH + AES-256 + Mutual Auth)
PHASE 2: CLIENT SIDE
1. Inputs : CAN (1D-Conv) | V2X (MLP) | GPS/IMU (1D-Conv)
2. Fusion : 10Hz Sync → FiLM Gating → 46-dim Vector
3. Model : KANConvNet
4. Train : SGD + L2 Regularization
5. Adapt : Personalization Blend (Global + Local)
6.Privacy : L2 Clip (C=1.0) + Gaussian Noise (σ=1.2)

## Slide 20: Baseline Architecture:
PHASE 3: SERVER AGGREGATION
1. Stage 1 : TOPSIS
Action : Dimensionality Reduction → Rank → Filter Outliers
3. Stage 2 : Multi-Krum
Action : Robust Clustering → Pairwise Distance → Average Top-m
PHASE 4: GA TUNING
1. Goal : Hyperparameter Optimization
2. Genes : {LR, Batch, Epochs, Momentum, Dropout, Optimizer, L2, α}
3. Flow : Init → Eval (F1) → Crossover → Mutate → Deploy

## Slide 21: KanConvNet Architecture:
STAGE 1: INPUT
1. Source : Fused Telemetry
2. Shape : 46-dim Vector
3. Preprocess : Normalization / Fourier Transform
STAGE 2: MAPPING
1. Logic : Linear Transform + Fourier Encoding
2. Sequence : Precedes Linear Summation
STAGE 3: ACTIVATION
1. Type : Kolmogorov-Inspired Nonlinearity
2. Placement : Network Edges
3. Benefit : High Interpretability / Safety Audits

## Slide 22: KanConvNet Architecture:
STAGE 4: HIDDEN LAYERS
1. Type : Intermediate Layers
2. Activation : ReLU
3. Goal : Spatial-Temporal Pattern Extraction
STAGE 5: OUTPUT
1. Map : Final Kolmogorov Activation
2. Classifier : SGD Prediction

## Slide 23: Why FHE in FL:

## Slide 24: Security and Performance Report:

## Slide 25: HE Scheme:
Scheme | Data Type | Top Strength | Main Limitation
BFV | Exact integers | Great for exact arithmetic and databases | Needs complex quantization for floats
BGV | Exact integers | Mature, strong integer support | Poor fit for float-valued model weights
CKKS | Approximate (Floats) | Best for neural networks & weighted sums | Requires careful error & parameter tuning
TFHE / FHEW | Bits / Boolean | Fast bootstrapping for small circuits | Way too slow for large vector aggregation
Hybrid | Mixed | Combines multiple schemes | High scheme-switching overhead
Threshold | Varies | Enables joint multi-party decryption | Unnecessary key-management complexity

## Slide 26: FINDINGS:
Fully HE Is Impractical in Our Scenario
Latency: Real-time IDS requires 10–100 ms response times, but FHE delays processing to seconds or minutes.
Hardware Constraints: Resource-heavy FHE drains batteries and starves safety applications on low-power On-Board Units.
Ciphertext Size: FHE expands model weights into gigabytes of data, saturating limited V2X wireless networks.
Mobility: Slow FHE aggregation means fast-moving vehicles will likely drive out of network range before updates complete.
Algorithmic Limits: Approximating essential non-linear IDS functions (like ReLU) with FHE triggers unsustainable computational overhead.

## Slide 27: Layered FHE
1. Full FHE encrypts all model parameters, making it too slow (seconds to minutes) and impractical for real-time IoV detection.
2. Layer-Wise FHE encrypts only the most sensitive layer of the KANConvNet model that captures vehicle-specific driving patterns.
3. All other layers (input, Fourier, activation, output) remain in plaintext to maintain speed and efficiency.
4. This approach maintains <60ms detection latency, keeps updates to kilobyte size, and runs on standard ECU-class hardware.
5. Key takeaway: Strong cryptographic privacy for critical vehicle data without sacrificing real-time performance.

## Slide 28: Work Completed:
1. KANConvNet Classifier
Architecture: Implemented with the Kolmogorov-Arnold trick (learnable edge activations via Fourier basis).
Custom Layers: Built FourierKANLinear, KolmogorovActivation, and KANConv1d modules.
Backbone: Configured a CNN backbone to process windowed vehicular sequences.
2. Data Pipeline & Preprocessing
Datasets: Integrated loaders for CAN-VTC, Car-Hacking, CICIDS 2017, and VeReMi.
Feature Engineering: Unified 46-feature extraction (timing, DLC, payload stats, CAN-ID histograms).
Normalization: Applied automated Z-score scaling and signal clipping.

## Slide 29: Work Completed:
3. Phase 1: Federated Setup
Distribution: Simulated realistic non-IID data via Dirichlet allocation (α=0.3) for 50-200 clients.
Security: Secured client-server channels with ECDH handshakes, AES-256-GCM, and mutual authentication.
Simulation: Built FederatedServer/Client classes and defined a Genetic Algorithm hyperparameter search space.
4. Infrastructure & Verification
Workflow: Built centralized train.py supporting full runs and rapid --smoke tests.
Orchestration: Automated the init sequence (partitioning → secure setup → broadcast) via phase1.py.
Validation: Integrated JSON training logs and best-weight checkpointing.

## Slide 30: Next Step
The project is now ready to move into Phase 2 (Federated Training), which involves implementing the TOPSIS + Multi-Krum aggregation logic and the Genetic Algorithm evolution loop.
We will look into the aggregate function and its mathematical formulation in detail to ensure proper implementation of the TOPSIS + Multi-Krum pipeline.