## Slide 1: Privacy-Preserving Collaborative IDS for Internet-of-Vehicle Networks
Thanking,
Dr. Durga
Dr. Uma
Dr. Anusuya
Dr. Praveen

## Slide 2: Recap from Last Meeting
ChebyKAN adopted as the IDS trunk — 44,164 parameters, 14× smaller than the MamKANformer trunk
Layer-wise homomorphic federated aggregation demonstrated across all four datasets
Committed to CKKS (FheFL) so the server never sees an individual plaintext update
Review action item: present the mathematical foundations of CKKS — addressed in this deck

## Slide 3: Contents
Mathematical foundations of CKKS
Baseline: FHE vs No-FHE — the control established before model quantization
System validation — proactive data-engineering validation
V2X communication protocol — FHE with AES / ECDH
Multi-key CKKS

## Slide 4: Where We Stand
Threat model, security specification, library evaluation, packing & encoding module, NTT reference implementation
Automated tests guarding data integrity, cryptographic correctness, and the privacy invariant — all passing
Real CKKS now replaces the placeholder throughout the federated loop
The homomorphic aggregator is implemented now

## Slide 5: Mathematical Foundations — The CKKS Scheme (worked example)

## Slide 6: Mathematical Foundations — Homomorphic Aggregation (worked example)

## Slide 7: Mathematical Foundations — Homomorphic Aggregation (worked example)

## Slide 8: Mathematical Foundations — Homomorphic Aggregation (worked example)

## Slide 9: Mathematical Foundations — Homomorphic Aggregation (Real CKKS case)

## Slide 10: Mathematical Foundations — Homomorphic Aggregation (Real CKKS Case)

## Slide 11: Mathematical Foundations — Noise, Depth, and Why It Shapes the Design
Every ciphertext carries growing noise; every ciphertext × ciphertext multiply consumes one prime ("level") from the modulus chain via rescaling
A chain of L primes supports L − 2 multiplications — the depth budget is the binding design constraint
Security is set by ring dimension N vs total modulus bits: at N = 8192, 128-bit security allows ≤ 218 bits → 2 multiplicative levels
Homomorphic addition is about 490× cheaper than ciphertext multiplication (measured)
Consequence: the FheFL protocol is engineered to need as few ciphertext × ciphertext multiplies as possible

## Slide 12: Baseline: FHE vs No-FHE — Setup
Purpose: the mandatory control before model quantization — measure what encryption costs before adding a second approximation
Real TenSEAL CKKS on one arm, exact plaintext on the other, everything else held identical
3 seeds · 10 simulated vehicles · 5 federated rounds · Dirichlet α = 0.3 · 70% client sampling
The two backends are asserted bitwise-identical on the aggregation path (test_backend_equivalence)

## Slide 13: Baseline: FHE vs No-FHE — Results
Dataset | CKKS acc | Plaintext acc | Δ | Verdict
CAN-VTC | 1.0000 | 1.0000 | +0.0000 | within seed noise
Car-Hacking | 0.9977 | 0.9981 | −0.0004 | within seed noise
CICIDS-2017 | 0.9555 | 0.9542 | +0.0012 | within seed noise
VeReMi | 0.4839 | 0.4851 | −0.0012 | within seed noise
Finding: encryption costs no accuracy — the CKKS/plaintext gap is smaller than seed-to-seed variance on every dataset
CAN-VTC = 100% is flood detection, not generalisation: the DoS attack floods one novel CAN ID (51% of traffic), separable by a single feature at 13σ. Split verified clean — the task is simply easy, not the earlier filename-label defect.
Car-Hacking is the CAN benchmark we stand behind: 5 real classes, best single feature only 0.94, injection density 12–24%
VeReMi is a near-chance lower bound: the cleaned export dropped sender IDs, so the misbehaviour signal cannot be expressed — re-acquisition required

## Slide 14: What This Baseline Establishes
Real CKKS now replaces the previous placeholder (SimulatedCKKSVector), so this is a controlled experiment for the first time
Accuracy is encryption-invariant → any accuracy change under INT8 quantization in now it is attributable to quantization alone
Measured cryptographic cost per client update (44k parameters): encrypt ~42 ms · encrypted distance ~118–230 ms · aggregation ~5–52 ms · wire size 2.47 MB

## Slide 15: System Validation — Proactive Data-Engineering Validation
Before building the multi-key layer, we ran a full validation pass over the existing pipeline: check the foundation before adding a floor
Seven issues identified and all fixed, each now covered by a regression test:
  Ground-truth labels now per-message (HCRL R/T flag), not per-file
  Train/test split now group-aware by contiguous block — no window leakage
  FHE vs No-FHE now a controlled comparison (real CKKS, bitwise-checked)
  Server no longer decrypts individual client updates — FheFL scoring replaces Multi-Krum
  Transport security (AES / ECDH) restored
  VeReMi formulation diagnosed (needs sender IDs); documentation drift corrected

## Slide 16: System Validation — Effect on Results and the Privacy Invariant
Headline accuracy figures were revised on the corrected pipeline: Car-Hacking 0.74 → 0.998 (fixed labels made the task well-posed); CICIDS 0.982 → 0.955 (leakage removed); CAN-VTC and VeReMi not comparable across formulations
These movements are the experiment starting to measure the right thing
Privacy invariant, machine-checked every round: individual client updates decrypted = 0 on all four datasets across 5 rounds each; only the aggregate is decrypted

## Slide 17: V2X Communication Protocol — FHE with AES / ECDH
Two complementary layers, not alternatives:
  FHE → payload confidentiality from the aggregation server
  AES-256-GCM / ECDH-P256 / Ed25519 → authentication, integrity, replay resistance, Sybil resistance on the radio link
FHE provides none of the second list; removing the channel in last time traded a working control for a slogan
Status: the transport channel is restored and integrated; mutual-auth handshake tested (test_secure_channel)

## Slide 18: V2X — The Bandwidth Problem
One 44k-parameter update = 2.47 MB encrypted (~915 DSRC frames); a 50-vehicle round ≈ 180 MB — does not fit a V2X budget
Delivered: Optimized Packing & Encoding module — 29.6% lossless reduction via level-dropped transmission, verified at zero accuracy cost
Further levers: seed compression (~50%, needs OpenFHE) · sparsification (needs an accuracy study) · hierarchical RSU pre-aggregation
Hierarchical aggregation is likely mandatory — an architecture decision to take early

## Slide 19: Why Multi-Key CKKS
Federated Learning keeps raw data on IoV devices, but individual model updates can still reveal private information.
Homomorphic Encryption (HE) allows the server to perform computations on encrypted model updates.
Single-key HE can create privacy risks because the same secret key may be shared/accessible across participants.
MK-CKKS gives each device its own secret key, improving key isolation.
However, the paper identifies a privacy leakage problem during individual decryption in MK-CKKS.
xMK-CKKS is proposed to protect individual model updates while still allowing secure aggregation.

## Slide 20: How xMK-CKKS Works
Each device generates its own secret key SiS_i and corresponding public key Pi
The public keys are combined to create an aggregated public key: P~=P1+P2+⋯+PN
Devices perform local training and encrypt their model updates using the aggregated public key.
The server performs homomorphic addition on the ciphertexts without seeing individual model updates.
The server obtains an encrypted aggregate and sends the required aggregate ciphertext information back to the devices.
Each device uses its secret key + aggregated ciphertext to generate a decryption share Di and sends it to the server.

## Slide 21: How xMK-CKKS Works

## Slide 22: How xMK-CKKS Works

## Slide 23: How xMK-CKKS Works

## Slide 24: Secure Aggregation & Benefits
The server combines the decryption shares with the aggregated ciphertext to recover only the sum of model updates.
The server computes the new global model using
Federated Averaging: Wt+1=1/N∑Wi
Individual updates W1,W2,…,WNremain protected from the server under the paper's threat model.
xMK-CKKS is designed to resist collusion between the server and k<N−1 participating devices.

## Slide 25: Status and the upcoming works to be done
Ciphertext serialization & comms protocol: partial — authenticated transport channel complete; serialization + fragmentation spec open
Model quantization: not started — encryption-neutral accuracy baseline now established as the control
On-device inference engine / embedded executable: pathway defined via the OpenFHE + C++ core migration
Future plan:
  OpenFHE migration — makes multi-key CKKS real rather than modelled
  Two one-line security fixes: bind round number into the AEAD (replay); enforce noise flooding in the deployment profile
  Low-magnitude persistent-poisoning experiment — the known blind spot in the scoring function
  Scale from 10 to 50 clients toward the roadmap target
  Re-acquire raw VeReMi with sender IDs